## Slide 1: Class A jitter scenario continued
Stein Gjessing
Bjornar Libaek
Petter Teigen
July 1. 2003
Basic scenario as yesterday,
see http://www.ifi.uio.no/~steing/rpr/sim_res.ppt

## Slide 2: Next page shows the STQ depth and Shaper D value of station 61
Top plot shows (in colour) how the 3% (30 Mbit/sec) class A traffic from stations 31 to 60 arrives at station 62 AND (in black) how the 1% (10 Mbit/sec) class A traffic from station 61 arrives at station 62.
Middle plot shows the shaper D value of station 61
Bottom plot shows the STQ size of station 61
Conclusion: Station 61 are not allowed to send A frames because the STQ is completely full!

## Slide 4: Now, shape secondary transit traffic with shaper D:
Modify condition in row 15 in table 6.29 to:
Frame = Dequeue(TX_STQ) && sendD != 0
Not shaping secondary transit when needy (spaceInSTQ < MTU_SIZE)
Not shaping PTQ Results on next page (notice that the STQ size is still only 12.5 Mbytes)

## Slide 6: Conclusions from previous page:
When shaper D shapes STQ, the STQ size increase faster (no surprise)
But shaper D still becomes negative when the STQ fills completely (because shaper D then does not shape STQ any more, shaper D is then only decreased)

## Slide 7: Now, increase STQ-size
Based on suggestion from Mike Takefman
STQ is now increased from 12.5KB to 256KB.
Still shaper D shapes STQ
Next page shows
  Top: Station 31 to 61 packets arrival at station 62 (notice the nice horizontal 10Mbit/s traffic (black line) from station 61)
  Bottom: STQ utilization in station 61
  Not shown: shaper D, which oscillates around normal values, and never becomes negative.

## Slide 9: Conclusion
With large STQs and shaping of STQ (by shaper D), class A jitter from station 61 is eliminated!
Still some jitter in the class A traffic from stations 31 to 60 To be further investigated